## Slide 1: Microcontrollers
Module 3: Digital Display

## Slide 2: 7 – Segment Display
A seven-segment display (SSD), or seven-segment indicator, is a form of electronic display device for displaying decimal numerals.
Seven-segment displays are widely used in digital clocks, electronic meters, and other electronic devices for displaying numerical information.

## Slide 5
DECIMAL POINT
Each of the segments A through G contains an LED that can be controlled individually

## Slide 6: 7-Segment LED Display Part Drawing and Pin Map
Pin No | Mapping
1 | Controls segment E
2 | Controls segment D
3 & 8 | Common Cathode
4 | Controls segment C
5 | Controls Decimal point
6 | Controls segment B
7 | Controls segment A
9 | Controls segment F
10 | Controls segment G

## Slide 7: 7-Segment Schematic
Each LED anode is connected to an individual pin. All the cathodes share a common connection, therefore, the 7-segment LED display can be called a “common cathode” display. By connecting either pin 3 or pin 8 to Vss, you will connect all the LED cathodes to Vss

## Slide 8: Lab Activity 1
Objective:To manually build a circuit and test each segment in a 7-segment display.
Background:In the first part of this activity, you will manually build a circuit with 7-segment display and resistors, and ensure that each segment lights when power is applied to that particular segment.
In the second part, you will display number‘3’and the letter ‘A’ using the 7-segment LED circuit.

## Slide 9
Equipment:
7-segment LED display
Resistors – 1 kΩ (brown-black-red)
Jumper wires
Procedure: Part A
With power disconnected from your Board of Education, build the circuit shown in Figure

## Slide 11
Reconnect power and verify that the A segment emits light.
Repeat the procedure for verifying different segments to emit light.

## Slide 12: Display a number
Build and test the circuit shown in the foll. Figure and verify that it displays the number three.

## Slide 15: Controlling 7 segment display using Basic Stamp
Objective:To build and control the 7-segment display LED circuit.
Background: In this activity, you will connect the 7-segment display to the BASIC stamp,
and then run a simple program to test and make sure each LED is properly connected.
The HIGH and LOW commands will accept a variable as a pin argument.
Therefore, they are placed in a FOR… NEXT loop, and index is used to set the I/O pin, high, then low again.

## Slide 16
Equipment:
7-segment LED display
Resistors – 1 kΩ (brown-black-red)
Jumper wires
Procedure:
Build the circuit shown in figure .

## Slide 18
Program and the BASIC Stamp by following the steps below:
Enter and run SegmentTestWithHighLow.bs2.
Verify that every segment in the 7-segment LED displays lights briefly, turning on and then off again.
Record a list of which segment each I/O pin controls

## Slide 20: Programming 7- segment display using Basic Stamp 2
Including the decimal point there are eight different BASIC Stamp I/O pins that send high/low signals to the 7-segment display.
That’s eight different HIGH or LOW commands just to display one number.
It requires more space in memory, so there are special variables used.

## Slide 21: DIRH and OUTH Variable.
DIRH VARIABLE
OUTH VARIABLE

## Slide 22: DIRH VARIABLE
DIRH Variable that controls the direction ( input or output ) of the pins P8 – P15
DIR – Short for direction
H – For high P8 – P15
DIRL – Also used. L – low for P0 – P7
Using DIRH Variable
DIRH = % 11110000

## Slide 23
DIRH = % 11110000
% - following means binary number
11110000 – Each bit corresponds to a pin in the following order.
% | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
PIN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
0 INPUT
1 OUTPUT
BACK

## Slide 24: OUTH VARIABLE
OUTH is a variable that controls the status of each output pin ( high or low ) for the pins P8 – P15
OUTH – HIGH ( P8 – P15 )
OUTL – LOW (P0 – P7 )
Using OUTH Variable
OUTH = % 11110000

## Slide 25
OUTH = % 11110000
% - following means binary number
11110000 – Each bit corresponds to a pin in the following order.
% | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
PIN | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
0 LOW
1 HIGH
BACK

## Slide 26: Using DIRH and OUTH commands
Look at the following commands now !
  OUTH = % 0 0 0 0 0 0 0 0
  DIRH = % 1 1 1 1 1 1 1 1
  The first command: OUTH = %00000000 gets all of the I/O pins (P8 through P15) ready to send the low signals.
  If they all send low signals, it will turn all the LEDs in the 7-segment display off.

## Slide 27
The I/O pins will not actually send the low signals until you use the DIRH variable to change all the I/O pins from input to output.
The second command: DIRH = %11111111 sets all I/O pins P8 through P15 to output.
As soon as this command is executed, P8 through P15 all start sending the low signal.

## Slide 28: Write the OUTH command for the figure shown.

## Slide 29
The picture shows number 3.
For displaying number 3 ,the following pins to be set high.
Refer the previous activity

## Slide 30
For displaying 3
      Make A B C D G as 1
      Make F E DP as 0
      From the figure we can write
      Hence the command is
      OUTH = % 11010110
P15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
B | A | F | G | DP | C | D | E
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0

## Slide 31: Look up command
Used to write code
The look up command lets you “ look up “ elements in a list.
It will help you select an item from the list, or compare an item to a list of items.
Command Syntax:
LOOKUP index, [item1, item2,…], value

## Slide 32: Example for LOOKUP command
LOOKUP index, [7, 85, 19, 167, 28], value
There are two variables used in this command, index and value.
INDEX | VALUE
0 | 7
1 | 85
2 | 19
3 | 167
4 | 28

## Slide 33: LOOKDOWN COMMAND
LOOKDOWN command compares a value with items in a list and informs the position (index)
It is the reverse of the LOOKUP command.
Command Syntax:
LOOKDOWN value, comparison[item1, item2,…], index

## Slide 34: Example for LOOKDOWN command
LOOKUP index, [7, 85, 19, 167, 28], value
There are two variables used in this command, index and value.
VALUE | INDEX
7 | 0
85 | 1
19 | 2
167 | 3
28 | 4

## Slide 35: PROGRAMMING WITH BASIC STAMP

## Slide 36
SOLUTION:
Since index is 2, in this example, the LOOKUP command places 19 into value, and that’s what the Debug Terminal displays.

## Slide 37: PROGRAMMING WITH BASIC STAMP

## Slide 38
SOLUTION
The value of index in this case would be “3”.